## Slide 1: Intrinsec, An intrinsically secure processor
Olivier SAVRY, Thomas HISCOCK, Mustapha EL MAJIHI, Sylvain BOULME, Paolo TORRINI

## Slide 2: An Avalanche of vulnerabilities
WHY ?
SECURITY IS NOT ANTICIPATED
SECURITY SKILLS ARE DIFFICULT, RARE AND EXPENSIVE
EVEN FOR EXPERTS, IT IS DIFFICULT TO DEAL WITH CERTAIN VULNERABILITIES
Gotlib

## Slide 3
LET’S START FROM A BASIC EXAMPLE
  Module 1 authenticates Module 2
Module 1
Module 2
Authentication
Module 2
Module 1
Authentication
APPLICATION PROCESSOR
k
k
SECURE ELEMENT
k
Authentication
s
s
Implementation of security functions in the Application Processor is finally necessary
SECURE APPLICATION PROCESSOR
k
THE DIFFICULTY TO DESIGN A SECURE SYSTEM (FOR IOT, CPS…)
Another way : design a secure application processor for embedded systems
A « plug and secure » processor : the developper just has to compile without worrying about vulnerabilities
IntrinSec : a family of Intrinsically Secure Application Processors for IoT and CPS
Notes: Pour bien comprendre les problèmes auxquels fait face un concepteur de systèmes sécurisés, prenons un peu exemple.
Admettons, qu’on a un système où un module 1 doit identifier un module 2, c’’est une problématique classique qu’on rencontre dans les systèmes où des modules sont mis en réseau par exemple dans une voiture, ou pour du contrôle d’accès.
Si on zoome sur le module 1, on va avoir un cœur d’application (typiquement un mcu) qui gère ce que le module doit faire. Et en particulier il va devoir gérer cette authentification avec par exemple un challenge response et donc un algo de crypto et une clé secrète k.
C’est là que les pb de sécurité arrivent: comment je protège cette clé et mon algo de toutes les attaques connues.
Le premier réflexe est de se dire: faisons appel à un Secure Element qui gèrera la sécurité pour le compte du cœur principal. Donc le SE fait tourner effectivement proprement l’algo de chiffrement dans les règles de l’art et stocke la clé k avec toutes les protections adéquates (au mieux qu’on sache le faire).
Toutefois, un problème de taille subsiste: on peut très bien prendre la main sur la communication entre SE et cœur d’application ou même changer le SE par un SE que l’on maitrise et qui se contente de dire au cœur que le module 2 est authentifié.
Pour lever ce problème, il faut que le cœur d’application authentifie le SE et donc à nouveau il faut implémenter un algo de crypto dans le cœur principal et stocker une clé de crypto. Vous voyez qu’on est revenu à peu près au point de commencement. On a gagné un petit peu en sécurité mais pas tant que cela.
Un plus serait de mettre le cœur d’application et le SE dans un même SOC. Mais cela n’éviterait pas que l’on puisse modifier le programme principal pour contourner le SE. Il faut donc mettre des contrôle d’intégrité, un secure boot, sur le processeur, avec une signature et donc un algo de chiffrement asymétrique plutôt lourd. Et encore ceci n’empêche pas de faire des modifs après le démarrage comme les basiques buffer overflows.
En conclusion de cette petite expérience de pensée, on voit que dans tous les cas on est obligé d’implémenter des fonctions de sécurité dans le processuer d’application. Pour répondre aux enjeux de la cybersécurité, on a essayé de faire un panorama des besoins des industriels pour leurs produits , produits qui peuvent aller d’un objet connecté à un CPS comme une voiture, un avion, une chaîne de production …

## Slide 4: STATE OF THE ART ON PROCESSORS VULNERABILITIES
An exhaustive survey of vulnerabilities of processors and the different exploitation techniques

## Slide 5: PROCESSORS VULNErABILITIES
Spectre & Meltdown
cache side-channel
Flush + Reload
Prime + Probe
Flush + flush
Cachebleed
Evict + Time
TLB
SRAM Memory:
Cell to cell coupling -> sofware fault injection in cache memories with transistors < 10 nm
DRAM Memory:
RowHammer
DRAMA
FLASH Memory
bit to bit
program interference with MLC
Power Management:
DVFS Exploitation : CLKScrew
FAULT INJECTION

## Slide 6: CONFIDENTIALITY, AUTHENTICITY AND INTEGRITY OF DATA AND INSTRUCTIONS
An holistic approach to address most threats with as few countermeasures as possible
Authenticated encryption of data and instructions is the way :
  To provide confidentiality against coldboot, reverse engineering, to protect software IP
  To provide authenticity and integrity against software or data modifications, faults injection in the memory hierarchy, faults injection during runtime
« Encrypt then MAC » structure
Integrity tag
MAC
Instruction or data
Ciphered by k, IV
Error Correcting Code
Integrity tag
MAC
Instruction or data
Ciphered by k, IV
Integrity tag
MAC
Instruction or data
Ciphered by k, IV
Error Detecting Code
Error Correcting Code
Random access ensures with IV=Constant || @
Heavy scheme but enables lots of security functions

## Slide 7: INTRINSEC : ENCRYPTION INTEGRATION IN RISC V PULPINO
RI5CY 32 bit core On FPGA (Xilinx Zynq 7020)
Debug Locker
Address filter
lock
APB slave to:
Set 128 Bits password
Verify password
Lock/Unlock
Carefull use of PMP for M-mode only access
Encryption Blocks

## Slide 8: AUTHENTICATED ENCRYPTION DESIGN : REQUIREMENTS
Encrypt then MAC with 128 bit key, 64 bits MAC
Lightweight and low latency design
Cipher/decipher with the same block
Encrypt instructions and data of programs
Support associated data
Memory adressing, alignment
compatible with operating systems (load/store of code lines, moving pages in physical memory,…)
Compatible with already compiled binairies

## Slide 9: AUTHENTICATED ENCRYPTION DESIGN
To improve throughput, instructions/data are bundled by 4 group of 32 bits + metadata (mainly EDC) + MAC (64 bits)
256 bit memory alignment
Overhead of 100 % for memory size
DATA0
DATA1
DATA2
DATA3
32
32
32
32
METADATA
MAC
64
64

## Slide 10: AUTHEnticated ENCRYPTION WITH ASCON
ASCON sponge-based cipher : CAESAR finalist
128 bit key
128 bits ciphered data + 64 bits associated data + 64 bits tag
Required 40 * permutation p
Only one instance of p is implemented
The permutations are computed asynchronously in 4 CPU cycles
Fast + lightweight

## Slide 11: PROGRAM ENCRYPTION
Instr1
Instr2
…
…
…
BEQ rs1,rs2,@1
BB0 at @0
Ciphered with IV=@0
Ciphered with IV=@0+1
Ciphered with IV=@0+n-1
Ciphered with IV=@0+n
Instr’1
Instr’2
…
…
BB1 at @1
Ciphered with IV=@1
Ciphered with IV=@1+1
Conditional branches or jal or jalr
This encryption scheme is totally independent of the compiler, it can be done on any binairies

## Slide 12: PROGRAM ENCRYPTION WITH CFI (CONTROL FLOW INTEGRITY)
Ciphered with IV=@0
Ciphered with IV=@0+1
Ciphered with IV=@0+n-1
Ciphered with IV=@0+n
Instr’1 ⨁ MASK1
Instr’2 ⨁ p(MASK1)
…
…
BB1 at @1
Ciphered with IV=@1
Ciphered with IV=@1+1
Instr1 ⨁ MASK0
Instr2 ⨁ p(MASK0)
…
…
(BEQ rs1,rs2,@1) ⨁ pn(MASK0)
BB0 at @0
Conditional branches or jal
…
(loadMASK MASKBRANCH,MASK1)
⨁pn-1(MASK0)
A new instruction « loadMASK » is introduced by the compiler to set a MASK that will be used by the next jump to unmask the next BB
Modification of LLVM to include Masks and new instruction LoadMASK

## Slide 13: PROGRAM ENCRYPTION WITH CFI (CONTROL FLOW INTEGRITY)
Ciphered with IV=@0
Ciphered with IV=@0+1
Ciphered with IV=@0+n-1
Ciphered with IV=@0+n
Instr’1 ⨁ MASK1
Instr’2 ⨁ p(MASK1)
…
…
BB1 at @1
Ciphered with IV=@1
Ciphered with IV=@1+1
Instr1 ⨁ MASK0
Instr2 ⨁ p(MASK0)
…
…
(jalr rd,rs=@1) ⨁ pn(MASK0)
BB0 at @0
jalr
…
(loadMASK MASKBRANCH,MASK1)
⨁pn-1(MASK0)
Instruction « loadMASK » is enriched to retrieve a mask to a certain address and not only a static value.
LoadMASK MASKregister , @MASK
Management of Indirect Jump (JALR Jump and Link Register)
(loadMASK MASKBRANCH,@1-1)
⨁pn-1(MASK0)
MASK1
@1-1
Ciphered with IV=@1-1
Compatible with old uninstrumented binairies (the loader just have to set MASK register to 0) and with dynamic librairies
For function return, the mask to decipher at return address is simply pushed on the stack with the ra

## Slide 14: VERIFIED COMPILer
Coq : interactive theorem prover
CompCert : C compiler, verified in Coq
Verified compilation :
  CA : compiler (C → Asm)
  CS : C source program semantics
  AS : Asm program semantics
  sp : source program
proof goal: CS (sp) ~ AS (CA (sp))
IntrinSec : new CompCert backend
based on existing RISC-V one
abstract model of encryption and decryption
compiles C code to symbolically encrypted Asm
verification proof in progress
JAIF2019| SAVRY Olivier| 23/05/2019
Notes: IL n’y a pas que LLVM qui a été modifié, l’équipe de Verimag avec Sylvain Boulmé et Paolo Torrini a aussi enrichi le compilateur certifié CompCert pour Risc v.
Compcert assure de façon formelle que la semantique du C est respectée.

## Slide 15: CONCLUSION
Confidentiality, authenticity and integrity of data and instructions on the memory hierarchy
100 % overhead on memory
No more need of secure boot
High degree of compatibility
  with old binairies (encryption independent of compilation)
  With dynamic librairies,
  With OS
LLVM, CompCert modified compilers to include CFI
  Introduction of new instruction implies an overhead of 15% on the code size.
Proof of concept on FPGA with RISC V Pulpino

## Slide 16: FUTUre challenges
Protection of the pipeline against fault injection
Protection of the pipeline against side-channel leakages
Resilience when attacks are performed
Intrinsic spatial and temporal memory safety
Implementation on 64 bit processors (Ariane ?)
Development of multitasks OS : freeRTOS, Linux with intrinsic isolation of processes

## Slide 19: Planche de pictos
capteurs
Imaging sensor
Serveurs et calcul intensif
sécurité
Dispositifs médicaux
Internet des objets
rf
Énergie électronique de puissance
Composants photonique
Nano electronique